PROGRAM DEALLOC
  This sample program sends an AST to a process deallocating a device
  which that process has allocated.

  Required privileges:
     CMKRNL  - To run kernel mode routine FORCE_DEALLOCATE
     WORLD   - To queue AST to target process.

  Example run:
     $ RUN DEALLOC
       Device to deallocate:  MUA0
       PID of process which has device allocated: 23C0011C
     $

  WARNING:
  Part of this program executes in kernel mode at elevated IPL which
  means any programming error which manifests itself at that time will
  cause the system to crash.  Keep that posibility in mind when
  initially testing this program on your system.  This program has been
  developed and tested on VMS 5.3

  For further information see:
     "VAX/VMS Internals and Data Structures" chapter on AST Delivery
     "VMS Device Support Manual"

David W. Deley   November, 1990
=============================================================================
Documentation of VMS internal routines used by this sample program:

NOTE:  The PID referred to in below descriptions may mean either EPID or IPID.

       The usual PID value such as obtained from the DCL command SHOW
       PROCESS or SHOW USERS/FULL is the value stored in the Process
       Control Block (PCB) field PCB$L_EPID and is referred to as EPID,
       or the Extended PID.

       The other PID value is the value stored in the Process Control
       Block (PCB) field PCB$L_IPID and is referred to as IPID, or the
       Internal PID.  (The low word of this value is used by the system
       as an index into the PCB vector table SCH$GL_PCBVEC)

-----------------------------------------------------------------------------


AST CONTROL BLOCK (ACB)
-----------------------------------------------------
|                      ASTQFL                       |
-----------------------------------------------------
|                      ASTQBL                       |           RMOD bits
-----------------------------------------------------        7 6 5 4 3 2 1 0
|    RMOD    |    TYPE    |          SIZE           |       | | | | | | |   |
-----------------------------------------------------        K Q N P s s  M |
|                        PID                        |        A U O K p p  O
-----------------------------------------------------        S O D A a a  D
|                        AST                        |        T T E S r r  E
-----------------------------------------------------          A L T e e
|                      ASTPRM                       |            E
-----------------------------------------------------            T
|                       KAST                        |            E
-----------------------------------------------------

The Asynchronous System Trap Control Block (ACB) describes a pending AST
for a process.  An AST is linked into a process's PCB by procedure SCH$QAST.

Fields:
ASTQFL - AST queue forward link reference
ASTQBL - AST queue backward link reference
SIZE   - Length (in bytes) of non-paged memory block this AST is in
TYPE   - Type of memory block
RMOD   - bits <0:1> (ACB$V_MODE) contain the value corresponding to the
                    access mode in which the AST routine is to execute.
                    Valid binary values for this field are:
                         PSL$C_KERNEL  = 00
                         PSL$C_EXEC    = 01
                         PSL$C_SUPER   = 10
                         PSL$C_USER    = 11
         bit <4> (ACB$V_PKAST) when set, indicates the presence of a
                    piggyback "special" kernel mode AST.
         bit <5> (ACB$V_NODELETE) when set, indicates that the non-paged
                    memory containing this ACB should not be deallocated
                    after the AST finishes executing.
         bit <6> (ACB$V_QUOTA) when set, indicates that the process AST
                    quota, PCB$W_ASTCNT, has been charged for this ACB.
         bit <7> (ACB$V_KAST) when set, indicates the presence of a special
                    kernel mode AST.  Note a special kernel mode AST
                    is entered via a JSB instruction instead of a standard
                    CALLG instruction.  IPL=2 upon entry of a special
                    kernel mode AST.  It is the responsibility of a special
                    kernel mode AST code to deallocate the non-paged memory
                    it is contained in upon completion, usually by loading
                    R0 with the ACB address and then finishing with a
                    JMP G^EXE$DEANONPAGED instruction.  At the end of
                    EXE$DEANONPAGED is a RSB instruction which acts as
                    the return from the AST.

PID    - The internal IPID of the target process to queue this AST to.
AST    - The address of the AST code entry point.  If the AST code follows
         immediately after the ACB header shown above, then this address
         may be calculated as the ACB base address + ACB$K_LENGTH.
         (If this is a special kernel mode AST, then this field is not
         used.  The address of a special kernel mode AST routine is placed
         in the KAST field below.)
ASTPRM - The value placed here is passed along to the AST routine as 4(AP).
KAST   - For special kernel mode routines only, the address of the special
         kernel mode AST entry point.  If the special kernel mode AST code
         follows immediately after the ACB header shown above, then this
         address may be calculated as the ACB base address + ACB$K_LENGTH.

-----------------------------------------------------------------------------


Routine EXE$NAMPID in module SYSPCNTRL in facility SYS

Description:
EXE$NAMPID obtains the proper [internal] PID and PCB address for a
standard process control service argument list consisting of an
[external] PID/process-name pair.  The absence of both selects the
current process.  After any necessary name translation and PID
validation, group and world process control privileges are checked.

Calling sequence:
     JSB EXE$NAMPID

Input Parameters:
     4(AP) - Address of PID source/destination (extended PID)
             (Must be writable or SS$_ACCVIO status is returned.)
     8(AP) - Pointer to process descriptor to convert to PID
             (not used by this example program)
     R4    - our PCB address (set for us by SYS$CMKRNL.  See description
             of SYS$CMKRNL)

Implicit Inputs:
     @SCH$GL_PCBVEC - Vector of PCB addresses.  (This is a system global
                      variable, always present)
     PHD$L_PRIV     - Privilege bit vector in process header.  (If you
                      do not have sufficient privilege to modify the
                      target process, EXE$NAMPID returns with status
                       SS$_NOPRIV.)

Output Parameters:
     If R0 EQL SS$_NORMAL  (the case we are interested in):
     R0     - SS$_NORMAL
     R1     - Internal process identification (IPID) of named process
     R2,R3  - Modified, used for scratch registers
     R4     - PCB address of target process
     @4(AP) - Extended process id (EPID) of selected process if 4(AP) <> 0
                 (This is also where we input the extended PID of the
                 target process we are interested in.)
     IPL = IPL$_SCHED

     If R0 EQL SS$_REMOTE_PROC:
     R0 - SS$_REMOTE_PROC
     R1 - EPID of process if PID <> 0, o otherwise
     R2 - CSID of remote node
     R3 - Modified, used for scratch register
     R4 - PCB address of current process
     IPL = 0

     If R0 is anything else:
     R0      - Status code
     R1-R4   - Undefined
     @4(AP)  - Undefined (might have been written!)
     IPL     - IPL$_SCHED (IPL unchanged if SS$_ACCVIO or SS$_IVLOGNAM)

Completion Codes:
     SS$_NORMAL - Normal successful completion.  (R1 contains IPID)
     SS$_REMOTE_PROC - EPID points at valid remote node (R2 contains CSID)
     SS$_IVLOGNAM - Invalid logical name string
     SS$_NONEXPR - Nonexistent process or invalid PID
     SS$_NOPRIV - No privilege for specified operation
     SS$_ACCVIO - Access violation for write destination

Discussion:
     For our example program here, we JSB to EXE$NAMPID with 4(AP) set
     to the external PID of our target process.  We expect a return
     status of SS$_NORMAL, in which case R1 is set to the internal IPID
     of our target process, and IPL is set to SCHED.

-----------------------------------------------------------------------------


Routine SCH$QAST in module ASTDEL in facility SYS

Functional Description:
SCH$QAST inserts the AST control block supplied in the proper position
by access mode in the AST queue of the process specified by the PID
field of the AST control block.  An AST arrival event is then reported
for the process to reactivate from a wait state if appropriate.  The
AST control block will be deallocated if the PID specifies a
non-existent process and the ACB$V_NODELETE bit in the ACB$B_RMOD
field of the AST header is not set.

(Note that the PID mentioned here is the internal PID of the
process corresponding to the PCB$L_IPID in the Process Control
Block which is different from the PCB$L_EPID External PID
field which is what the user normally sees with a SHOW PROCESS
or SHOW USERS command.  The low word of the internal PID value here
is used as an index into the PCB vector table SCH$GL_PCBVEC.
It must be within proper range of internal PID values or
SCH$QAST may result in an access violation which crashes the
system.)

Calling Sequence:
     JSB SCH$QAST

Input Parameters:
     R2 - Priority increment class
     R5 - Pointer to AST control block

Implicit Inputs:
     PCB of process to queue AST to is identified by ACB$L_PID field
     in AST header.  This field contains the internal PID (IPID) value
     of the target process.

Output Parameters:
     R0 - Completion status code
     R4 - PCB address of process for which AST was queued

Side Effects:
     The process identified by the PID in the AST control block
     will be made executable if not suspended.

Completion Codes:
     SS$_NORMAL  - Normal successful completion status
     SS$_NONEXPR - Non-existent process

-----------------------------------------------------------------------------


Routine EXE$ALONONPAGED in module MEMORYALC in facility SYS
(Also documented in "VMS Device Support Manual")

Description:
This routine is called to allocate a block of memory from
the nonpaged pool.

Inputs:
     R1 = Size of block requested in bytes.

Outputs:
     R0 = Return status.  SS$_NORMAL or SS$_INSFMEM if memory not available.
          If success status then:
          R1 = actual size of allocated block
          R2 = address of allocated block

Note:  Don't drop IPL below ASTDEL while we have nonpaged pool allocated.
       Otherwise our process may be deleted and the nonpaged pool will be
       lost forever.
       (However, we can never be deleted while in a special kernel mode
       AST since no other AST can squeeze in front of a special kernel
       mode AST.  Thus a special kernel mode AST may drop IPL to 0 even
       though it enters at IPL=2.)

-----------------------------------------------------------------------------
Routine EXE$DEANONPAGED in module MEMORYALC in image SYS$SYSTEM:SYS.EXE

Description:
     This routine is called to deallocate a block of memory to
     the nonpaged pool.

Inputs:
     R0 = Address of block to be deallocated
     IRP$W_SIZE(R0) = Size of block to be deallocated
     IRP$B_TYPE(R0) = Type of block to be deallocated

     Note:  It is assumed that there is a standard header at the
            beginning of the block of memory to be deallocated.
            Note that the header for an AST Control Block (AST) is
            identical to the header for an I/O Request Packet (IRP).
               Thus:  IRP$W_SIZE = ACB$W_SIZE
                      IRP$B_TYPE = ACB$B_TYPE

Side effects:
     The specified block is returned to nonpaged pool.

-----------------------------------------------------------------------------



OTHER NOTES:
 1.  No page faults are allowed when IPL is above IPL$_ASTDEL.  All code
     and data that might be referenced while at elevated IPL must be locked
     in memory.

 2.  Any unhandled exception (i.e. an unexpected oops) while in kernel
     mode will cause the system to crash.  Establishing a crash handler
     works only as long as the process is at or below IPL$_ASTDEL.
     When IPL is above IPL$_ASTDEL, the system crashes anyway.  Since
     all of our kernel mode routine FORCE_DEALLOCATE executes at
     IPL$_SCHED, we don't establish a crash handler.

 3.  Don't drop IPL below ASTDEL while we have nonpaged pool allocated.
     Otherwise our process may be deleted and the nonpaged pool will be
     lost forever.
     (However, we can never be deleted while in a special kernel mode
      AST since no other AST can squeeze in front of a special kernel
      mode AST.  Thus a special kernel mode AST may drop IPL to 0)


 4.  Other system routines to look into (not used in this sample program):

     a.  SCH$RWAIT in module MUTEX in facility SYS.  This routine is
         used to place a procedure into a resource wait state.

     b.  EXE$EXCMSG in module EXCEPTMSG in facility SYS.
         This routine prints a stack dump of the current process state.
         It can be called by an exception handler to print a stack dump.

-----------------------------------------------------------------------------


OUTLINE OF DEALLOC PROGRAM

The program starts at .ENTRY MAIN.  Our first task is to obtain the name
of the device to deallocate and the PID of the target process to send
the AST to.  The name of the device to deallocate is prompted for and
stored in DEVBUF.  (DEVBUF is in the AST code and data section because
the AST routine will reference it later.)  The PID of the process to
queue the AST to is then prompted for.  The string response is stored in
INPUTBUF.  This is then converted from hexadecimal text to an integer and
stored in TARGET_PID.  (Note that fancier code could automatically
determine the PID of the process which has the device allocated given
the device name in DEVBUF.)

Having obtained the device name and PID of the target process, we
prepare to call the kernel mode routine FORCE_DEALLOCATE.  We lock in
memory all pages of code and data accessed at elevated IPL.  The entire
kernel mode routine FORCE_DEALLOCATE executes at elevated IPL, and it
access the AST code and data while at elevated IPL.  We lock into memory
the kernel mode code and the AST code and data.

We then call our kernel mode routine FORCE_DEALLOCATE, passing to it a
prefabricated argument list NAMPID_ARGLST.  This argument list contains
2 arguments, the first argument is the address of TARGET_PID, the second
argument is not used (it's there as a place holder).

Routine FORCE_DEALLOCATE calls EXE$NAMPID.  This system routine raises
IPL to SCHED and converts the external EPID (TARGET_PID) referenced by
4(AP) to an internal IPID value which it returns in R1.  We temporarily
store this IPID value in R6.

We then call EXE$ALONONPAGED to allocate a block of non-paged memory for
the AST.  (Note that fancier code would enter a resource wait state at
this point if EXE$ALONONPAGED returned with SS$_INSFMEM.  See routine
SCH$RWAIT in module MUTEX in facility SYS.)

Having allocated a block of non-paged memory, we proceed to fill it in
creating an AST Control Block (ACB).  The first 7 longwords of the ACB
is header information.  Included in the ACB header is the size of our
non-paged memory block, the type of block, the access mode for the AST
routine to execute in, the IPID of the target process to queue this AST
to, and the address of the AST routine entry point.  If the AST code
immediately follows the header, the AST routine entry point address is
calculated as the ACB base address + ACB$K_LENGTH which is the length of
the ACB header.

The AST code and data is then copied to the memory block.  It is placed
immediately after the ACB header.

Also, now that we know the base address of our non-paged memory block,
we can calculate the absolute address of data within the memory block. 
DALLOC_ARGLST is an argument list passed to SYS$DALLOC.  It consists of
two arguments.  The first argument is the address of the string
descriptor DEVICED which contains the name of the device to deallocate. 
We calculate and fill in this address.  The DEVICED descriptor itself
contains the address of DEVBUF which we also calculate and fill in.
(Note that earlier this address was correct when the device name string
was prompted for and stored.  Now that we have moved everything to
non-paged memory, the address is no longer correct.)

With the AST completely built, we queue it to the target process by
calling SCH$QAST.  We then reset IPL to 0 and return with status in R0.

When the target process receives the AST, it puts on hold whatever it
was doing and executes the AST routine.  After executing the AST routine
it resumes whatever it was doing.  If we're lucky, we'll find that the
target process has deallocated the device as we wanted it to.

More than likely though, somewhere along the line the system will crash
instead due to a bug in this program.  See file ANALYZE_CRASH.DOC for help
in analyzing a system crash to determine where the program went wrong.

This program has been developed and tested on VMS 5.3