FRAGMENT and DEFRAG

FRAGMENT and DEFRAG are programs which assist in transferring very large
files over flaky telephone lines.  The idea is to create a backup save
set of the files you want to transfer, run FRAGMENT to break the big
backup save set file into many little files, transfer all the little
files using kermit set to FILE TYPE FIXED with a wildcard filename, run
DEFRAG to reconstruct the backup save set file from all the little
files, and recover all the files you wanted to transfer from the backup
save set.  This way if the phone line flakes out during one of the file
transfers, you haven't lost everything you've achieved up to that point.


The FRAGMENT program takes a large file consisting of fixed length
32256 byte records and breaks it into a number of smaller files
consisting of fixed length 512 byte records.  The smaller files
have names of the form filename.001, filename.002, filename.003,
etc.  You specify the block size of the output files.  The smaller
files can then be transferred via kermit using the SET FILE TYPE
FIXED command and wildcard transfer mode.  The original file can
then be pieced back together by running the DEFRAG program.

Here is an example of how to transfer a number of files:
   1.  Backup all the files you want to transfer into a backup
       save_set using the command:
         $ BACKUP [MYDIR]*.* MYSAVSET.BCK/SAVE_SET/BLOCK_SIZE=32256

   2.  Run this program.
         $ RUN FRAGMENT
         INPUT FILE: MYSAVSET.BCK
         OUTPUT FILE (minus type and version): MYFRAGSET
         OUTPUT FILE BLOCK SIZE: 25

   3.  Transfer the files.
         Kermit> SET FILE TYPE FIXED  !Set on receiving end
         Kermit> SEND MYFRAG.*

   4.  Piece back together the original save_set on remote node.
         $ RUN DEFRAG
         INPUT FILE (minus type and version): MYFRAG
         OUTPUT FILE: MYSAVSET.BCK